## Slide 1: EE 210
LECTURE 1
CIRCUIT VARIABLES
Cenk Efeler
Reference Book :Electric Cırcuits
James W.Nielson & Susan A.Riedel

## Slide 2: ELECTRICAL SYSTEMS
Communication Systems
Computer Systems
Control Systems
Power Systems

## Slide 3: Communication Sytems
Communication Systems enable transfer of information between different users.
Examples of communication systems are TV’s,VCR’s,radios,DVD players,Digital video receivers,mobile phones and radar systems.
Communication systems include a coder, a transmitter ,a communication channel ,a receiver and a decoder.

## Slide 4: Computer Systems
Computer systems make use of electric signals to process information for various purposes such as word processing,computer aided design,accounting ,climate simulations and mathematical operations.

## Slide 5: Control Systems
Control systems use electric signals to control processes such as the control of temperatures and pressures in chemical plants,aircraft and missile guidance,motor speed control .

## Slide 6: Signal Processing Systems
Signal processing systems convert electric signals into more useful forms.Signal processing is applied in a wide range of areas such as human speech processing,image and video processing,radar signal processing,seismic signal processing.

## Slide 7: CIRCUIT THEORY
An electric circuit is a mathematical model of an electrical system.
An electric circuit can physically represent a tiny circuit in an integrated circuit on a silicon chip or a power distribution system km’s long.
Cicuit theory can also be used to model mechanical systems by replacing the electrical components with their mechanical equivalents.
Commonly the term electric circuit is used to refer to both the physical electrical system and its mathematical model.

## Slide 8: CIRCUIT THEORY ASSUMPTIONS
1-Electrical effects happen almost instantaneously due to the fact that electrical signals travel near the speed of light.Thus,if the system is small relative to the wavelength of electric signals,we can assume the same effect everywhere in the circuit.These systems are called lumped-parameter systems.
2-No component can collect net charge. A capacitor collects charge,but its charge is zero.It holds equal and opposite charge.
Magnetic coupling can only occur within a component not between the components in a circuit.

## Slide 9: The International System Of Units
Quantity Basic Unit Symbol
Length meter m
Mass kilogram kg
Time second s
Electric Current ampere A
Thermodynamic temperature kelvin K
Amount of Substance mole mol
Luminous Intensity candela cd
Frequency hertz(Hz) 1/s
Force newton(N) kg.m/s*s
Energy or Work joule (J) N.m
Power watts(w) J/s
Electric Charge coulombs(C) A.s
Electric Potential Volt(V) J/C
Electric Resistance ohm V/A
Electric Conductance siemens(s) A/V
Electric Capacitance farad(F) C/V
Magnetic Flux Weber(wb) V.s
Inductance henry(H) wb/A

## Slide 10: Stardized Prefixes to Signify Powers of 10
Prefix Symbol Power
atto a
Femto f
pico p
nano n
Micro
Milli m
Centi c
Deci d
Deca da
Hecto h
Kilo k
Mega M
Giga G
Tera T

## Slide 11
Circuit design starts with design specifications.
Mathematical model for electrical systems is a circuit model.
Elements of the circuit model are ideal circuit elements.
An ideal circuit element should represent the behaviour of the actual electrical component to an acceptable accuracy.
CIRCUIT ANALYSIS

## Slide 12: CIRCUIT ANALYSIS
1-Design specifications => Desired Circuit Behaviour
2-Circuit Analysis => Predicted (Theoretical Behaviour)
1 and 2 are compared, if they are in agreement a physical prototype can be constructed.The physical prototype is an actual electrical system, constructed from physical electrical components.
If the behaviour of the physical prototype is in agreement with the design specifications and the the predicted circuit behaviour of circuit analysis,the physical system is implemented.

## Slide 13: CIRCUIT ANALYSIS
If the circuit analysis results do not agree with the design specifications, refinements may be needed in the physical prototype, the circuit model or both.
The iteration between the physical prototype and the design spefications and the circuit analysis continues until the behaviour of the physical prototype meets both the design requirement specifications and the circuit analysis results.

## Slide 14: CIRCUIT ANALYSIS
DESIGN SPECIFICATIONS
CIRCUIT MODEL
PHYSICAL PROTOTYPE

## Slide 15: VOLTAGE AND CURRENT
Electrical charge is the basis for understanding the current.
Characteristics of Electrical Charge
1-Charge is bipolar, it is either positive or negative.
2-Charge is quantized,meaning that it can exist only as integer multiples of unit charge,the magnitude of the electron charge: C.
3-Electrical effects are caused either by the seperation or motion of charges.Seperation of charge causes an electric force and a voltage.The motion of charge causes an electric fluid (current).

## Slide 16: The Ideal Basic Circuit Elements
The assignment of the reference polarity for voltage and current and their reference direction are arbitrary.However,once you have assigned the references,you must write all subsequent equations accordingly.
Widely used convention is the passive sign convention : when the current is assigned in the direction from positive to negative terminal,the sign of the voltage must be positive,which also implies that when the voltage polarity is given,the current must be assigned in the direction from positive to negative terminal. Example 1.3 – 1.4

## Slide 17: VOLTAGE AND CURRENT
Voltage : The Energy per unit charge created by the separation.We express this ratio as v=dw/dq
v = The voltage in volts
w = The energy in joules
q = The charge in coulombs
Current : The rate of charge flow is the electrical current: i = dq/dt
i = The current in amperes
q = The charge in coulombs
t = The time in seconds.

## Slide 18: VOLTAGE AND CURRENT
Polarity reference + or – should be assigned to these variables due to the bipolar nature of the charge.
Allthough current contains large number of descrete electrons, it is considered continous.Physical components are modeled based on the voltage and current at their terminals,thus two physically diferent components which have the same voltage and current at their terminals are considered identical in the circuit model.

## Slide 19: The Ideal Basic Circuit Elements
An ideal circuit element has three attributes
1-It has only two terminals
2-It is described in terms of its voltage and current
3-It is the basic unit,it cannot be divided further into smaller components.
Basic circuit elements are the building blocks for constructing circuit models, they themselves however cannot be modeled with any other type of element.

## Slide 20: POWER AND ENERGY
Since all electrical devices have power limitationsi in the circuit design process in addition to the voltage and current,we need to compute the power as well.Power is the time rate of change of energy.
P=dw/dt p: Power in watts
w : The energy in joules
t : The time in seconds.
Thus 1 W = 1 J/s.

## Slide 21: POWER AND ENERGY
Power is associated with a pair of terminals,its sign indicates whether the power is delivered to the circuit element or whether the power is absorbed from the circuit element.This information automatically comes when the passive sign convention is followed.
The sign of power is related to the movement of the charges through the terminals of a circuit element.

## Slide 22: POWER AND ENERGY
Power and energy of a circuit element
i
i
i
i
a) P=vi
b) P=-vi
c) P=-vi
d) P=vi
+
+
+
+
-
-
-
-
v
v
v
v
1
1
1
1
2
2
2
2

## Slide 23: POWER AND ENERGY
If positive charges move from positive to negative terminal of a circuit element a voltage drop occurs,thus leading to an energy loss in the charges.If the positive charges move from negative to positive terminal of a circuit element,a voltage rise occurs resulting in an energy gain in the charges.
Energy loss of charges means, energy is being transferred or delivered to the circuit element,resulting in a positive power with respect to the circuit element.Energy gain of charges means that the power is absorbed from the circuit element resulting in a negative power with respect to the circuit element. Example 1.5 Example 1.6