## Slide 1: EE 210
LECTURE 2
CIRCUIT ELEMENTS
Cenk Efeler
Reference Book :Electric Cırcuits
James W.Nielson & Susan A.Riedel

## Slide 2: ELECTRICAL SOURCES
An electrical source is a device that can convert any form of energy other than the electrical energy to electrical energy and the electrical energy to other forms of energy.

## Slide 3: ELECTRICAL SOURCES
DYNAMO : A dynamo can convert mechanical energy to electrical energy or electrical energy to mechanical energy.
Mechanical Electrical
Energy Energy
If a dynamo is operated in the mechanical to electric mode,it is called a generator.If converting from electrical to mechanical energy,it is called motor.
DYNAMO

## Slide 4: ELECTRICAL SOURCES
These electrical sources either deliver or absorb electric power,generally maintaining either a constant voltage or current.This leads to the creation of ideal voltage or current sources as the basic circuit elements.

## Slide 5: IDEAL ELECTRICAL SOURCES
An ideal voltage source is a circuit element that maintains a constant voltage across its terminals irrespective of the current that flows through it.An ideal current source is a circuit element that maintains a constant current through its terminals irrespective of the voltage across its terminals.
vs is
+
_
a)
b)

## Slide 6: DEPENDENT & INDEPENDENT SOURCES
Ideal voltage and current sources can further be classified as dependent or independent sources.
An independent source supplies a voltage or a current that does not depend on any of the voltages and currents elsewhere in the circuit.A dependent source,however,supplies a voltage or current whose value depends on the value of a voltage or current elsewhere in the circuit.

## Slide 7: DEPENDENT & INDEPENDENT SOURCES
A dependent source is shown with a diamond symbol and can be controlled either by a voltage source or by a current source.
As there two types of sources:voltage and current there are four possible combinations.
+
_
+
_
is a dimensionless constant
has dimensions amperes per volt
is a dimensionless
constant
has dimensions volts per ampere

## Slide 8: ACTIVE AND PASSIVE CIRCUIT ELEMENTS
Ideal circuit elements are active circuit elements.An active circuit element represents a device that provides energy and a passive element represents a device that is either consuming energy or simply storing and releasing back the existing energy in the circuit.Resistors dissipate energy,capacitors and inductors store or give back the energy.Resistors,capacitors and inductors are passive circuit elements.Voltage and current sources are active circuit elements.

## Slide 9: SAMPLE ELECTRONIC DEVISES(CIRCUIT ELEMENTS)

## Slide 10: ACTIVE DEVICES
An active device is any type of circuit component with the ability to electrically control electron flow (electricity controlling electricity). In order for a circuit to be properly called active, it must contain at least one active device. Active devices include, but are not limited to, vacuum tubes, transistors, silicon-controlled rectifiers (SCRs), and TRIACs.

## Slide 11: PASSIVE DEVICES
Components incapable of controlling current by means of another electrical signal are called passive devices. Resistors, capacitors, inductors, transformers, and even diodes are all considered passive devices. A diode is shown below.

## Slide 12: ELECTRICAL RESISTANCE
Resistance is the capability of materials to withstand the flow of electric current, or the flow of electronic charges. The circuit element that models the resistance of a material is called resistor.The symbol of resistance is R.
R

## Slide 13: ELECTRICAL RESISTANCE
As current flows through a circuit element,electrons collide with the atoms of the material in which they travel and their kinetic energy is converted to thermal energy.As different materials have different atomic structures, the number of collisions the same number of electrons experience per unit distance varies from material to material.Therefore,resistance varies from material to material,it is a material specific parameter.

## Slide 14: ELECTRICAL RESISTANCE
Two possible reference choices for the current and voltage at the terminals of a resistor.
+
+
_
_
i
i
v
v
R
R
V=iR
V=-iR
Figure1
Figure2

## Slide 15: ELECTRICAL RESISTANCE
The current in the resistor must be referenced to the terminal voltage.We can do this either as in Figure 1,by assigning the current in the direction of the voltage drop or as in Figure 2,by assigning it in the direction of voltage rise.
In the first case the voltage is: 1-v=iR and in the second case 2-v=-iR.
Where v = The voltage in volts,
i = The current in amperes
R = The reistance in ohms.

## Slide 16: OHM’S LAW
These algebraic signs for both cases above are the direct results of passive sign convention and the above equations 1 and 2 are known as Ohm’s law.
Expressing the current as the function of voltage:

## Slide 17: OHM’S LAW
The reciprocal of the resistance i s referred to a conductance,it is symbolized by G,and is measured in the units of Siemens (S).
S
In circuit analysis ideal resistors are used.An ideal resistor is a resistor whose resistance value does not change with time.Most actual devices have resistance values that change with time.

## Slide 18
The power at the terminals of a resistor (power consumed by the resistor) can be computed in several ways.
1- p = vi ,when v=iR or p=-vi when v=-iR depending on the reference.
2-Expressing the power at the terminals of a resistor in terms of the current and the resistance.
THE POWER AT THE TERMINALS OF A RESISTOR

## Slide 19: THE POWER AT THE TERMINALS OF A RESISTOR
The above results indicate that regardless of voltage polarity and current direction,the power at the terminals of a resistor is positive.Therefore,a resistor always absorbs power from the circuit.
3- The power at the terminals of a resistor can also be expressed in terms of the voltage and resistance:

## Slide 20: THE POWER AT THE TERMINALS OF A RESISTOR
It is also possible to express the resistor value as a conductance rather than a resistance.In that case the power becomes:
Depending on the type of information available in the problem one of the above equations can be used. Example 2.3-Assessing Object 2.3

## Slide 21: KIRCHOFF’S LAWS
Ohm’s law may not always provide a complete solution for the circuit.In that case we apply Kirchoff’s laws.
Definition of Node:
A node is a point
where two or more
circuit elements
meet. In the circuit
a,b,c,d are
nodes
+
_
a
c
b
_
+
+
_
+
_
d

## Slide 22: KIRCHOFF’S LAWS
For the above circuit there are 7 unknowns.7 equations are needed to solve for these unknowns.3 of these equations comes from Ohm’s law.
The remaining four equations come from Kirchoff’s current law.
Kirchoff’s Current Law : The algebraic sum of all the currents at any node in a circuit equals zero.A reference direction must be assigned to every current prior to applying Kitchoff’s current law.

## Slide 23: KIRCHOFF’S LAWS
When entering currents are assigned a positive sign,then leaving currents must be assigned a negative sign and when leaving currents are assigned a positive sign,then entering currents must be assigned a negative sign.
node a :
node b :
node c :
node d :

## Slide 24: KIRCHOFF’S LAWS
Only three of the above equations are independent,that is any one of the above equations can be written as a linear combination of the remaining three.
Kırchoff’s Voltage Law : Prior to defining Kirchoff’s voltage law,we must define what a closed path is.A closed path (a loop) is generated by starting at an arbitrary node of the circuit and returning to the original node without passing through any intermediate node more than once.The circuit given above has one close path.

## Slide 25: KIRCHOFF’S LAWS
Kirchoff’s Voltage Law : The algebraic sum of all the voltages around any closed path in a circuit equals zero.
In order to use Kirchoff’s voltage law,we must assign an algebraic sign (reference polarity) to each voltage in the closed path.(loop)
Applying Kirchoff’s voltage law to the circuit example above:

## Slide 26: KIRCHOFF’S LAWS
Now we have 7 equations,but we can simplify these equations first by using Ohm’s law,which says that if either the current or voltage is known across a known resistor,the other quantity voltage or current can be determined.This enables the elimination of the unknown voltages: v1,vc and vl.
We are now left with 4 equations and 4 unknowns.One more simplification helps reduce the number of unknowns.

## Slide 27: KIRCHOFF’S LAWS
Kirchoff’s current law says that when only two elements are connected to a node,if the current in one element is known,the current in the other element can be computed.
This implies that only one unknown current is defined for the two elements.Such elements connected to a single node are said to be connected in series.With this simplification the four equations involving the four unknown currents reduce to a single equation.

## Slide 28: Examples
Example 2.6 Using Kirchoff’s Laws – KCL
Example 2.7 Using Kirchoff’s Laws – KVL
Example 2.8 Application of Kirchoff’s Laws
Assessing Objective 2

## Slide 29: ANALYSIS OF CIRCUITS CONTAINING DEPENDENT SOURCES
Dependent Sources:Consider the circuit below:
500 V
+
_
+
_
b
c

## Slide 30: ANALYSIS OF CIRCUITS CONTAINING DEPENDENT SOURCES
Our goal is to determine the unknown voltage
across the resistor,using Kirchoff’s laws and Ohm’s law.
We make the following observation to develop a strategy to solve the circuit.
Once is determined, can be computed from Ohm’s law.
Once is computed,the value of the dependent source can be determined.
The current in the 500V source is

## Slide 31: ANALYSIS OF CIRCUITS CONTAINING DEPENDENT SOURCES
There are two unknown currents and .Two linearly independent equations containing these unknown currents are needed.
Applying Kirchof’s voltage law around the closed path a,b,c
Equation 1:
Now if we if we attempt to write a second Kirchoff’s voltage law equation for the closed path b,c,we see that the resulting equation will contain two unknowns and v and thus will not lead to a solution.

## Slide 32: ANALYSIS OF CIRCUITS CONTAINING DEPENDENT SOURCES
Instead we write Kirchoff’s current law equation at either node b or node c.Selecting node b,we obtain a second equation involving the two unknown currents.
Equation 2 :
Solving the equations 1 and 2 for and we get
A A
We use Ohm’s law to find the voltage
V

## Slide 33: ANALYSIS OF CIRCUITS CONTAINING DEPENDENT SOURCES
Important result of this problem:Not every closed path and not every node provides a useful equation to reach the solution,we must think and analyze the circuit before writing Kirchoff’s voltage law and Kirchoff’s current law equations.

## Slide 34
Example 2.10 Assessing Objective 2.9-2.10