## Slide 1: EE 210
LECTURE 3
SIMPLE RESISTIVE CIRCUITS
Cenk Efeler
Reference Book :Electric Cırcuits
James W.Nielson & Susan A.Riedel

## Slide 2: RESISTORS IN SERIES AND IN PARALLEL
To analyze more complex circuits than the circuits studied in Chapter 1 and 2,they need to be reduced into smaller ,simpler circuits called equivalent circuits.
In this chapter we will consider circuits which contain only resistors and constant voltage or constant current sources. Such sources are called direct current : d.c sources. The equivalent circuits of these circuits will be obtained by simplifying the resistor combinations.

## Slide 3: RESISTORS IN SERIES
Figure 1
Figure 1: Circuit of resistors connected in Series.
When two circuit elements are connected to a single node,they are considered to be connected in series.
Series connected resistors carry the same current.
+
a
b
c
d
h
g
e
f
vs
R1
R2
R3
R4
R7
R6
R5
i1
i2
i3
i4
i7
i6
i5
is
_

## Slide 4: RESISTORS IN SERIES
This can be shown using Kirchoff’s Current Law.
Node a
Node b
Node c
Node d
Node e
Node f
Node g

## Slide 5: RESISTORS IN SERIES
Combining all these equations:
Which basically says that if one of the currents are known,all others can be computed.

## Slide 6: RESISTORS IN SERIES
+
_
a
b
c
d
h
g
e
f
vs
R1
R2
R3
R4
R7
R6
R5
is
is
is
is
Figure 2
Circuit of resistors in series with a single current.

## Slide 7: RESISTORS IN SERIES
The circuit containing seven resistors in series can be replaced by an equivalent circuit containing a single equivalent resistor.
Figure 3
_
+
is
vs

## Slide 8: RESISTORS IN SERIES
Applying Kirchoff’s current law:
Or
And

## Slide 9: RESISTORS IN PARALLEL
Two circuit elements connected at a single node pair are considered parallel.The voltage across parallel connected circuit elements is the same.
Figure 4
Circuit of resistors connected in parallel.
a
b
is
i2
i3
i4
i1
vs
+
_
R1
R2
R3
R4

## Slide 10: RESISTORS IN PARALLEL
In order to be connected in parallel the same voltage must exists across the two circuit elements
Circuit 1 Circuit 2
Figure 5
R1 and R2 in circuit 1 are connected in parallel,but R1 and R2 or R1 and R3 in circuit 2 are not connected in parallel, as the voltages across them are different.
R1
R2
R3
R2
R1

## Slide 11: RESISTORS IN PARALLEL
Using Kirchoff’s current law and Ohm’s law,resistors in parallel can be reduced to a single equivalent circuit.
Writing Kirchoff’s current law equation at node a :
As the voltage across each resistance is the same,applying Ohm’s law
Thus

## Slide 12: RESISTORS IN PARALLEL
Substitiuting these relationships for currents into the kirchoff’s current law equation:

## Slide 13: RESISTORS IN PARALLEL
Thus the four resistors in parallel can be replaced by a single equivalent resistor and an equivalent circuit can be drawn.
Figure 6
In terms of conductances
_
+
vs
a
b
is
Req

## Slide 14: RESISTORS IN PARALLEL
When only two resistances are connected in parallel.
Figure 7
a
b
R1
R2

## Slide 15: RESISTORS IN PARALLEL
When only three resistances are connected in parallel.
Figure 8
a
b
R1
R2
R3

## Slide 16: Example 3.1

## Slide 17: THE VOLTAGE DIVIDER & THE CURRENT DIVIDER CIRCUITS
Voltage Divider Circuit
Figure 9
_
+
_
+
R1
R1
R2
R2
vs
vs
v1
v2
v2
v1
+
+
+
+
-
-
-
-
I

## Slide 18: THE VOLTAGE DIVIDER CIRCUIT
The circuit analysis results show that the voltages across the resistors connected in series are equal to the source voltage,that is the total voltage on the resistances times the ratio of the resistance to the equivalent resistance of the resistors connected in series:the total resistance of all resistors.
Consider now a different circuit where a load resitance RL has been connected in parallel to the second resistance of the above circuit.

## Slide 19: THE VOLTAGE DIVIDER CIRCUIT
Circuit with load resistance in parallel.
R1 and R2 has been replaced with a single equivalent resistance
Figure 10
vs
v0
R1
R1
Req
R2
RL
+
_
+
_
vs
+
_
+
_
v0

## Slide 20: THE VOLTAGE DIVIDER CIRCUIT
We obtain
Substituting Req into the equtaion of V0
As long as the voltage
ratio is not effected by the load
resistance

## Slide 21: Example 3.2

## Slide 22: THE CURRENT DIVIDER CIRCUIT
The Current Divider Circuit.
The circuit is designed to divide the current is into currents i1 and i2.
Figure 11
Using Ohm’s Law :
R1
R2
i2
is
i1
v
+
_

## Slide 23: Example 3.3

## Slide 24: VOLTAGE DIVISION & CURRENT DIVISION
The generalization of voltage and current division circuits leads to two new circuit analysis techniques known as voltage division and current division.
Figure 12
…..
…..
R1
R1
Rn
Rj
Rn-1
Circuit
+
_
vj
+
_
v
i

## Slide 25: VOLTAGE DIVISION & CURRENT DIVISION
The box on the left can contain a single voltage source or a combination of basic circuit elements that cause a voltage v.
To the right of the box there are n resistors connected in series.
We would like to determine the voltage drop across any of the resistors above.
We first find the current using Ohm’law:
where

## Slide 26: VOLTAGE DIVISION & CURRENT DIVISION
The above result is the voltage division formula applied to a voltage across any resistor Rj.It states that the voltage across any resistor is simply the product of the ratio of that resistance to the total equivalent resistor and the voltage source v.Thus the voltage across a resistor is proportional to that resistor’s ratio to the total resistance.

## Slide 27: VOLTAGE DIVISION & CURRENT DIVISION
Figure 13
Circuit
i
ij
+
_
v
R1
R2
Rj
…..
…..
…..
…..
Rn-1
Rn

## Slide 28: VOLTAGE DIVISION & CURRENT DIVISION
Now we consider the circuit of parallel connected resistors above.Similiar to the voltage division example,the box on the left side can be a current source or any combination of circuit elements.The resulting current is i.
We have n resistors connected in parallel and we are interested in finding the current ij in any of these resistors.
Using Ohm’s law:

## Slide 29: VOLTAGE DIVISION & CURRENT DIVISION
We apply Ohm’s law once more to calculate the current ij through the resistor Rj.
The equation above is the current division equation.The current in any of the resistors Rj is equal to the product of the total current and the ratio of the equivalent parallel resistance to Rj.Thus the current in any resistor is proportional to the parallel equivalent resistor’s ratio to that resistor.
We note that the constant of proportionality in the current division equation is the inverse of the constant in the voltage division equation.

## Slide 30: Example 3.4

## Slide 31: MEASURING VOLTAGE & CURRENT
An ammeter is an instrument that measures the current and a voltmeter is an instrument that measures the voltage.
An ammeter is connected in series with the circuit element whose current is being measured.
A voltmeter is connected in parallel with the circuit element whose voltage is being measured.

## Slide 32: MEASURING VOLTAGE & CURRENT
Figure 14
An ammeter connected to measure the current in R1 and a voltmeter connected to measure the voltage across R2.
R1
R2
vs
V
A

## Slide 33: MEASURING VOLTAGE & CURRENT
Figure 15 İdeal ammeter and ideal voltmeter
A short circuit model for the ammeter and an open circuit model for the voltmeter.
R1
R2
vs
V
A
+
_

## Slide 34: MEASURING VOLTAGE & CURRENT
An ideal ammeter has an equivalent resistance of 0 ohm and thus appears as a short circuit.
An ideal voltmeter has infinite equivalent resistance thus appears as an open circuit.

## Slide 35: MEASURING RESISTANCE THE WHEATSTONE BRIDGE
Figure 16 The Wheatsone Bridge Circuit
v
+
_
R1
R2
R3
Rx
a
b
c
d
İ3
İ2
İx
İg
İ1

## Slide 36: MEASURING RESISTANCE THE WHEATSTONE BRIDGE
The Wheatstone bridge is typically used to measure resistances in the range of 1 to 1 within 0.1 % accuracy.The bridge consists of a dc voltage source,usually a battery,four resistances,one of which R3 can be varied and a current detector (an ammeter) between nodes a and b.
R1,R2 and R3 are known resistances,Rx is the unknown resistor.

## Slide 37: MEASURING RESISTANCE THE WHEATSTONE BRIDGE
Applying Kirchoff’s Current Law at node a amd b
When the bridge is balanced,there is no voltage drop across the detector.In this case writing Kirchoff’s voltage law equations we get:
Equation 1 Equation 2

## Slide 38: MEASURING RESISTANCE THE WHEATSTONE BRIDGE
Combining with Kirchoff’s current law equations
Equation 3 :
Solving for the ratio in both Equations 3 and 2 and setting them equal we get

## Slide 39: Assessing Objective 3.7

## Slide 40: DELTA –TO-WYE (PI-TO-TREE) EQUIVALENT CIRCUITS
The bridge configuration above presents an interconnection of resistors that requires further investigation.
Replacing the galvanometer with its equivalent resistance Rm,the wheatstone bridge circuit above can be redrawn as below.
Figure 17
A resistive network generated by a wheatstone bridge circuit.
v
+
_
R1
R2
Rx
R3
Rm

## Slide 41: DELTA –TO-WYE (PI-TO-TREE) EQUIVALENT CIRCUITS
The resistance across the terminals of the battery cannot be reduced to a single equivalent resistor,using series or parallel resistance combinations alone.
The interconnected resistors can be reduced to a single equivalent resistor by means of a delta-to-wye
( to y) or pi-to-tee ( to T ) equivalent circuit.
The resistors R1,R2 and Rm (or R3,Rm and Rx) in the circuit above are referred to as delta İnterconnections because the interconnection looks like the greek letter
. This configuration is also known as pi interconnection because the can be shaped into a without disturbing the electrical equivalence of the two configurations.

## Slide 42: DELTA –TO-WYE (PI-TO-TREE) EQUIVALENT CIRCUITS
A Configuration viewed as Configuration
Figure 18
Rb
Rc
Ra
Ra
Rb
Rc
a
c
b
a
b
c

## Slide 43: DELTA –TO-WYE (PI-TO-TREE) EQUIVALENT CIRCUITS
The resistors R1,Rm and R3 (or R2,Rm and Rx) in the Figure 17 are referred to as y İnterconnection.The y configuration is also called as T interconnection,because the y structure can be shaped into a T structure without dsiturbing the electrical equivalence of the two structures.
Figure 19 A Y structure viewed as a T structure
R1
R3
R3
R1
R2
R2
b
a
a
c
b
c

## Slide 44: DELTA –TO-WYE (PI-TO-TREE) EQUIVALENT CIRCUITS
Figure to Y transformation
Rb
Ra
Rc
R1
R2
R3
a
b
c
a
b
c

## Slide 45: DELTA –TO-WYE TRANSFORMATION
The equivalent resistors of both configurations along the paths ab,bc and ca can be written and set equal to eachother.




## Slide 46: DELTA –TO-WYE TRANSFORMATION
From algebraic manipulations:
Reversing the to Y transformation is also possible.We can start wit the Y structure and replace it with an equivalent structure.The expressions for the three - connected resistors are:

## Slide 47: WYE –TO – DELTA TRANSFORMATION
Wye – to – delta transformation.

## Slide 48: Example 3.7